## Slide 1: Tree Canopy Coverage Mapping of Signal Mountain and Walden
Johnathan Smith
Dr. Azad Hossain
Geology 4550: Remote Sensing
April 22nd, 2024

## Slide 2: Problem Statement
The city of Signal Mountain and Walden do not have the capability, time, and/or budget to acquire tree canopy coverage statistics as often as they would like.
Tree canopy coverage has been said to be declining within the city limits previously and is a concern for multiple reasons, including urban heat islands, biodiversity loss, and land value loss.

## Slide 3: Goals and Objectives
This project intends to show the tree canopy coverage of both Signal Mountain and Walden via remote sensing.
This will be accomplished through image classification and dot grid analysis techniques using ArcGIS Pro and ERDAS Imagine.
In this analysis I will find three distinct classes of coverage for each image in both data analysis techniques. My intention is for the results to be of use to Signal Mountain Tree Board.

## Slide 4: Data Acquisition
Tennessee City Boundary Shapefile acquired from the State of Tennessee GIS website via the Office of the Comptroller.
Rastered data was acquired from Sky Sat with two dates across four images. Acquired imagery had a 0.5 x 0.5 meter resolution across four spectral bands of red, green, blue, and NIR.
  Set 1 from September 27, 2021
  Set 2 from May 12, 2022
The rastered data was previously pansharpened prior to use. All data acquired was confirmed to be of the same source, projection, and resolutions.

## Slide 5: Study Site
Map shown displays the cities of Signal Mountain and Walden via Sky Sat imagery.
Shapefile shown was acquired from the State of Tennessee Office of the Comptroller.

## Slide 6: Methodology – Creating the Raster
For this project the first steps were isolating Signal Mountain and Walden cities into one layer from the larger Tennessee shape file. Once that was done, all four rastered images were clipped separately using that shape file.
The “Mosaic to New Raster” tool in ArcGIS Pro was used to combine all four rastered images into one. This new rastered image would be used for dot grid analysis.

## Slide 7: Sky Sat Image Mosaic and Clip
Signal Mountain
Walden
Quirk of using two different datasets gathered at two different times. This was accounted for in analysis.
To the right is the image used for the dot grid analysis. Signal Mountain and Walden are listed for ease of reference.

## Slide 8: Methodology – Dot Grid Analysis
The dot grid analysis was conducted entirely within ArcGIS Pro with the “Create Fishnet” tool. I used the Signal Mountain and Walden shapefile as a template extent. Cell widths were set at 3/16 of a mile (301.73 meters) as that was proven more accurate according to the previous project on Signal Mountain tree canopy coverage.
After changing symbology to help workflow, the feature layer was clipped to the previous shapefile before being manually inspected for 3 classes:
  Pervious Surfaces
  Impervious Surfaces
  Tree Canopy Coverage

## Slide 9: Methodology – Unsupervised Classification
Performed “K-means” unsupervised classification on unaltered rastered images independently in ERDAS Imagine. This was done at a 95% confidence interval over ten maximum iterations each.
Manual inspection using both true color and false color composite NIR imagery allowed classification into four classes initially. These four classes were:
  Pervious Surfaces
  Impervious Surfaces
  Tree Canopy Coverage
  Water Coverage

## Slide 10: Methodology – Unsupervised Classification
Due to a lack of accuracy from one set of data due to the time of day it was taken casting shadows, classification was lowered to the following classes:
  Pervious Surfaces (now including water coverage)
  Impervious Surfaces
  Tree Canopy Coverage
The data was then assessed for accuracy using true color maps and world topographic maps before each being recoded.
Data was imported into ArcGIS Pro where it was clipped to the shapefile and turned into a new raster via the mosaic function.

## Slide 11: Dot Grid Analysis
The dots’ colors have been altered to aid in visualization.
The data shows 336 points at a width of 3/16 of a mile.
Pervious Surfaces: 17.96% (60)
Impervious Surfaces: 13.98% (47)
Tree Canopy Coverage: 68.15% (229)

## Slide 12: K-Means Analysis
The map to the right shows the K-means unsupervised classification and recoding at 0.25 square meter resolution.
Pervious Surfaces: 19.63% (~6.05 square kilometers)
Impervious Surfaces: 8.71% (~2.68 square kilometers)
Tree Canopy Coverage: 71.66% (~22.08 square kilometers)

## Slide 13: Results
The results show similar results across the two methods of analysis. One point to note is that of the Impervious Surfaces class having a large disparity between K-means and dot grid. The difference represented showed K-means at 62.3% of the total impervious coverage of dot grid.
The results are mostly consistent with the prior project if we combine the pervious and impervious surfaces into one class for comparison.
 | Sky Sat 2021/2022 | 2021 NAIP | 2018 TDOT | 2010 TDOT
Unsupervised Classification | C: 71.66% I: 28.34% | C: 73.8% I: 26.2% | C: 74.26% I: 25.74% | C: 76.9% I: 23.1%
Dot Grid Analysis | C: 68.15% I: 31.94% | C: 59.38% I: 40.62% | C: 60.42 % I: 39.58 % | C: 68.75% I: 31.25%

## Slide 14: Conclusions
I believe that the results show a further reduction in tree canopy coverage in both unsupervised classification and in dot grid analysis.
While the K-means unsupervised classification is quite clearly a drop from 73.8% to 71.66%, if the previous project had followed the 3/16 per mile cell width and had three classes I am sure the results would show a higher tree canopy coverage as it most definitely has not increased.

## Slide 15: Discussion
I would stress acquiring one raster image in the future, rather than splicing as that led to issues with classification and analysis.
Further change detection analysis using three classes instead of two could show a difference not just in tree canopy coverage, but in pervious surfaces becoming impervious surfaces.
NDVI was not used as in the time I had to assess its accuracy it was much less accurate at detecting ground vegetation versus canopy than either dot grid or K-means. This led to abandonment as I had not intention of using only two classes.
I would recommend using NAIP imagery in conjunction with LIDAR to train for height maps to better assess for canopy coverage in the future.
Notes: https://www.sciencedirect.com/science/article/pii/S1618866717304508?casa_token=k-EsLX7T8JQAAAAA:Bqe_9VQRW5Q5JPbtXq1NlKwMjG7VrkPGj28B_Bn2Ukc3UeBY91crtDamtJK4sm50yspjep6LN6Wq https://www.mdpi.com/2071-1050/13/13/7496 https://www.sciencedirect.com/science/article/pii/S0921800922000866?casa_token=Viy1ZlQ0-lIAAAAA:7FPS6VeZr2JkQ2mURfL-1JiSJmVFU7aumWLF3GMZgg6DbX-ww54wOJPUnA1YDe_xkZHhsv5snKwL https://www.sciencedirect.com/science/article/pii/S1618866721003927